365 Days Program Timer

# MODEL Name: QCM-6600

*APPLICATIONS*

Security System, Auto Control System, Broadcast System Control, Energy-Saving /AD lights Control, Automatic Sprinkler / Fountain Control…

**FEATURE & SPECIFICATION***

  - Fully LCD display in Chinese.

  - Connect PC with RS-232 interface.  Set schedules, Synchronize time and download data via our free software

  - Provide 8 output triggers for setting

  - Provide 160 messages for each group of output trigger

  - Different schedules can be set on different weekdays

  - Same schedules can be set on each weekday

  - Provide 5 specified schedules for setting

  - All schedules can be set via LCD front panel / PC software

  - Contents of messages and RTCC will be hold when power failure

  - Show current time & date when in stand-by mode

  - External equipment --GPS module for time adjustment

HWAN MAW TECH. Co., Ltd.

E-mail : hmtsales@hmt.com.tw

TEL: 886-2-2274-1347